## Slide 1: LYRA on-board PROBA2
M. Dominique, I.E. Dammasch, L. Wauters, T. Kastiyannis
http://proba2.oma.be

## Slide 2: PROBA2: an ESA microsat
Launched on November 9, 2009
17 technology demonstrators + 4 scientific instruments
LYRA first light on January 6, 2010
Mission currently founded till end 2012. Extension procedure is on-going.
LYRA
SWAP

## Slide 3: PROBA2 orbit
PROBA2 orbit:
Heliosynchronous
Polar
Dawn-dusk
725 km altitude
Duration of 100 min
Occultation season:
  From October to February
  Maximum duration 20 min per orbit

## Slide 4: LYRA highlights
3 redundant units protected by independent covers
4 broad-band channels
High acquisition cadence: nominally 20Hz
3 types of detectors:
  Standard silicon
  2 types of diamond detectors: MSM and PIN
    radiation resistant
    blind to radiation > 300nm
Calibration LEDs withλof 370 and 465 nm

## Slide 5: Details of LYRA channels
Channel 1 – Lyman alpha
120-123 nm
Purity : ∼25%
Channel 2 – Herzberg
190-222 nm
Purity : ∼95%
Unit 1 | Unit 2 | Unit 3
MSM | MSM | Si
Unit 1 | Unit 2 | Unit 3
PIN | PIN | PIN
Channel 3 – Aluminium
17-80 nm + < 5nm
Purity : ∼97%
Channel 4 – Zirconium
6-20 nm + < 2nm
Purity : ∼95%
Unit 1 | Unit 2 | Unit 3
MSM | MSM | Si
Unit 1 | Unit 2 | Unit 3
Si | MSM | Si

## Slide 6: LYRA channels convolved with quiet Sun spectrum
Channel 1 – Lyman alpha
120-123 nm
Channel 3 – Aluminium
17-80 nm + < 5nm
Channel 2 – Herzberg
190-222 nm
Channel 4 – Zirconium
6-20 nm + < 2nm

## Slide 7: Filter + detector combined responsivity
Unit 1
Unit 2
Unit 3
Diamond cut-off
Bump in Si around 900nm
Bump in C around 220nm

## Slide 8: Example of LYRA data

## Slide 9: Data products
Data products and quicklook viewer on
http://proba2.oma.be

## Slide 10: Calibration
Includes:
Dark-current subtraction
Additive correction of degradation
Rescale to 1 AU
Conversion from counts/ms into physical units (W/m2)
ATTENTION: this conversion uses a synthetic spectrum from SORCE/SOLSTICE and TIMED/SEE at first light => LYRA data are scaled to TIMED/SORCE ones
Does not include (yet)
Flat-field correction
Stabilization trend for MSM diamond detectors

## Slide 11: Non-solar features in LYRA data
Large Angle Rotations
Flat field
LAR: four times an orbit
SAA affects more Si detectors independently of their bandpass
Flat-field: Proba2 pointing is stable up to 5arcsec /min (from SWAP). Jitter introduces fluctuations in the LYRA signal of less than 2%.

## Slide 12: Non-solar features in LYRA data
Occultation: from mid-October to mid-February
Auroral perturbation
  Only when Kp > 3
  Only affects Al and Zr channels independently of the detector type
  Does not affects SWAP (though observing in the same wavelength range)
Occultations

## Slide 15: Degradation
Status on February 15, 2016
Channel | Remaining signal
Unit 2 | 
Channel 2-1 | 0.6%
Channel 2-2 | 0.03%
Channel 2-3 | 3%
Channel 2-4 | 30%
Channel | Remaining signal
Unit 1 | 
Channel 1-1 | 62%
Channel 1-2 | 75%
Channel 1-3 | 100%
Channel 1-4 | 100%
Channel | Remaining signal
Unit 3 | 
Channel 3-1 | 61%
Channel 3-2 | 9%
Channel 3-3 | 19%
Channel 3-4 | 71%
=> Slow evolution

## Slide 16: Getting LYRA data

## Slide 17: Getting LYRA data: description

## Slide 18: Getting LYRA data: link to the data
… or
lyra_download_data and read_lyra/read_lyrametadata in SolarSoft
using sunpy.lightcurve in Python

## Slide 19: Getting LYRA data: quicklook viewer

## Slide 20: Quicklook viewer: nominal data

## Slide 21: Quicklook viewer: backup uncalibrated data

## Slide 22: Getting LYRA data: SolarSoft and SunPy

## Slide 23: Getting LYRA data: SolarSoft and SunPy

## Slide 24: Getting LYRA events

## Slide 25: Getting LYRA events

## Slide 26: Getting LYRA events
… or lyra_download_events and lyra_remove_event in SolarSoft

## Slide 27
Space weather monitoring

## Slide 28: Space weather monitoring

## Slide 29: Terms of use and acknowledgment